## Slide 1: 计算机组成与系统结构 Computer Organization & System Architecture
Huang Kejie (百人计划研究员)
Office: 玉泉校区老生仪楼304
Email address: huangkejie@zju.edu.cn
HP: 17706443800

## Slide 2
Everything is bits
Each bit is 0 or 1
By encoding/interpreting sets of bits in various ways
  Computers determine what to do (instructions)
  … and represent and manipulate numbers, sets, strings, etc…
Why bits? Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.2V
0.9V
1.1V
0
1
0

## Slide 3
Count in binary
Base 2 Number Representation
  Represent 1521310 as 111011011011012
  Represent 1.2010 as 1.0011001100110011[0011]…2
  Represent 1.5213 X 104 as 1.11011011011012 X 213

## Slide 4
Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 5
Binary Number Property
w = 0:
1 = 20
Assume true for w-1:
1 + 1 + 2 + 4 + 8 + … + 2w-1 + 2w = 2w + 2w = 2w+1
Claim
1 + 1 + 2 + 4 + 8 + … + 2w-1 = 2w
= 2w

## Slide 6
Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | − | − | 10/16
pointer | 4 | 8 | 8

## Slide 7
Illustration of a Representation Taxonomy
data types
bits
things being
represented
IEEE 754
single-prec.
non-negative
integers
integers
text
real
numbers
vegetables
unsigned
16-bit unsigned
signed- magnitude
2’s com-
plement
32-bit 2’s com-
plement
64-bit 2’s com-
plement
Unicode (16-bit)
ASCII
7-bit
ASCII
floating- point
fixed- point
representations

## Slide 8
Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
  Encode “True” as 1 and “False” as 0
And
A&B = 1 when both A=1 and B=1
Or
A|B = 1 when either A=1 or B=1
Not
~A = 1 when A=0
Exclusive-Or (Xor)
A^B = 1 when either A=1 or B=1, but not both

## Slide 9
Application of Boolean Algebra
Applied to Digital Systems by Claude Shannon
  1937 MIT Master’s Thesis
  Reason about networks of relay switches
    Encode closed switch as 1, open switch as 0
A
~A
~B
B
Connection when
A&~B | ~A&B
A&~B
~A&B
= A^B

## Slide 10
General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 11
Example: Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j ∈ A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 12
Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 ➙ 0xBE
    ~010000012 ➙ 101111102
  ~0x00 ➙ 0xFF
    ~000000002 ➙ 111111112
  0x69 & 0x55 ➙ 0x41
    011010012 & 010101012 ➙ 010000012
  0x69 | 0x55 ➙ 0x7D
    011010012 | 010101012 ➙ 011111012

## Slide 13
Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 ➙
  !0x00 ➙
  !!0x41 ➙
  0x69 && 0x55 ➙
  0x69 || 0x55 ➙
  p && *p
  0x00
  0x01
  0x01
  0x01
  0x01
  (avoids null pointer access)
Watch out for && vs. & (and || vs. |)…
one of the more common oopsies in
C programming

## Slide 14
Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
    Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on left
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 15
Encoding Integers
C short 2 bytes long
Sign Bit
  For 2’s complement, most significant bit indicates sign
  0 for nonnegative
  1 for negative
short int x = 15213;
short int y = -15213;
Unsigned
Two’s Complement
Sign
Bit

## Slide 16
Two-complement Encoding Example (Cont.)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011

## Slide 17
Numeric Ranges
Unsigned Values
  Umin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s Complement Values
  Tmin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
Other Values
  Minus 1
    111…1
Values for W = 16

## Slide 18
Values for Different Word Sizes
Observations
  |TMin | = TMax + 1
    Asymmetric range
  Umax = 2 * TMax + 1
C Programming
  #include <limits.h>
  Declares constants, e.g.,
    ULONG_MAX
    LONG_MAX
    LONG_MIN
  Values platform specific

## Slide 19
Unsigned & Signed Numeric Values
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
 Can Invert Mappings
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s comp integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7

## Slide 20
Mapping Between Signed & Unsigned
Mappings between unsigned and two’s complement numbers: Keep bit representations and reinterpret
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
U2T
U2B
B2T
Two’s Complement
Unsigned
Maintain Same Bit Pattern
ux
x
X

## Slide 21
Mapping Signed ↔ Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
U2T
T2U

## Slide 22
Mapping Signed ↔ Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
=
+/- 16

## Slide 23
Relation between Signed & Unsigned
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
ux
x
w–1
0
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X

## Slide 24
Bit-Level Operations in C
2’s Comp. → Unsigned
  Ordering Inversion
  Negative → Big Positive
0
TMax
TMin
–1
–2
0
UMax
UMax – 1
TMax
TMax + 1
2’s Complement Range
Unsigned
Range

## Slide 25
Proof
Unsigned
Two’s Complement

## Slide 26
Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux;
    uy = ty;

## Slide 27
Signed vs. Unsigned in C
Expression Evaluation
  If there is a mix of unsigned and signed in single expression, signed values implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32: TMIN = -2,147,483,648 , TMAX = 2,147,483,647
Constant1 | Constant2 | Relation | Evaluation
0 | 0U | == | unsigned
-1 | 0 | < | signed
-1 | 0U | > | unsigned
2147483647 | -2147483647-1 | > | signed
2147483647U | -2147483647-1 | < | unsigned
-1 | -2 | > | signed
(unsigned) | -2 | > | unsigned
2147483647 | 2147483648U | < | unsigned
2147483647 | (int) 2147483648U | > | signed

## Slide 28
Signed vs. Unsigned in C
Bit pattern is maintained
But reinterpreted
Can have unexpected effects: adding or subtracting 2w
Expression containing signed and unsigned int
  int is cast to unsigned!!

## Slide 29
Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X’ = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
• • •
X
X 
• • •
• • •
• • •
w
w
k
k copies of MSB

## Slide 30
Sign Extension Example
Converting from smaller to larger integer data type
C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 31
Integer C Puzzles
x < 0  ((x*2) < 0)
ux >= 0
x & 7 == 7  (x<<30) < 0
ux > -1
x > y  -x < -y
x * x >= 0
x > 0 && y > 0  x + y > 0
x >= 0  -x <= 0
x <= 0  -x >= 0
(x|-x)>>31 == -1
ux >> 3 == ux/8
x >> 3 == x/8
x & (x-1) != 0
int x = foo();
int y = bar();
unsigned ux = x;
unsigned uy = y;
Initialization

## Slide 32
Summary: Expanding, Truncating: Basic Rules
Expanding (e.g., short int to int)
  Unsigned: zeros added
  Signed: sign extension
  Both yield expected result
Truncating (e.g., unsigned to unsigned short)
  Unsigned/signed: bits are truncated
  Result reinterpreted
  Unsigned: mod operation
  Signed: similar to mod
  For small numbers yields expected behavior

## Slide 33
Unsigned Addition
Standard Addition Function
  Ignores carry output
Implements Modular Arithmetic
  s = UAddw(u , v) = u + v mod 2w
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
UAddw(u , v)

## Slide 34
Mathematical Properties
Modular Addition Forms an Abelian Group
  Closed under addition
    0  UAddw(u , v)  2w –1
  Commutative
    UAddw(u , v) = UAddw(v , u)
  Associative
    UAddw(t, UAddw(u , v)) = UAddw(UAddw(t, u ), v)
  0 is additive identity
    UAddw(u , 0) = u
  Every element has additive inverse
    Let UCompw (u ) = 2w – u UAddw(u , UCompw (u )) = 0

## Slide 35
Complement & Increment Examples
x = 15213
x = 0

## Slide 36
Visualizing (Mathematical) Integer Addition
Integer Addition
  4-bit integers u, v
  Compute true sum Add4(u , v)
  Values increase linearly with u and v
  Forms planar surface

## Slide 37
Visualizing Unsigned Addition
Wraps Around
  If true sum ≥ 2w
  At most once
0
2w
2w+1
UAdd4(u , v)
u
v
True Sum
Modular Sum
Overflow
Overflow

## Slide 38
Two’s Complement Addition
TAdd and UAdd have Identical Bit-Level Behavior
  Signed vs. unsigned addition in C:
int s, t, u, v;
s = (int) ((unsigned) u + (unsigned) v);
t = u + v
Will give s == t
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
TAddw(u , v)

## Slide 39
Mathematical Properties of TAdd
Isomorphic Group to unsigneds with UAdd
  TAddw(u , v) = U2T(UAddw(T2U(u ), T2U(v)))
    Since both have identical bit patterns
Two’s Complement Under TAdd Forms a Group
  Closed, Commutative, Associative, 0 is additive identity
  Every element has additive inverse

## Slide 40
Mathematical Properties of TAdd
Claim: Following Holds for 2’s Complement
  ~x + 1 == -x
Complement
  Observation: ~x + x == 1111…111 == -1
Complete Proof?
1
0
0
1
0
1
1
1
x
0
1
1
0
1
0
0
0
~x
+
1
1
1
1
1
1
1
1
-1

## Slide 41
TAdd Overflow
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
–2w –1
–2w
0
2w –1–1
2w–1
True Sum
TAdd Result
1 000…0
1 011…1
0 000…0
0 100…0
0 111…1
100…0
000…0
011…1
PosOver
NegOver
u
v
< 0
> 0
< 0
> 0
Negative Overflow
Positive Overflow
TAdd(u , v)

## Slide 42
Visualizing 2’s Complement Addition
Values
  4-bit two’s comp.
  Range from -8 to +7
Wraps Around
  If sum ≥ 2w–1
    Becomes negative
    At most once
  If sum < –2w–1
    Becomes positive
    At most once
TAdd4(u , v)
u
v
PosOver
NegOver

## Slide 43
Multiplication
Goal: Computing Product of w-bit numbers x, y
  Either signed or unsigned
But, exact results can be bigger than w bits
  Unsigned: up to 2w bits
    Result range: 0 ≤ x * y ≤ (2w – 1)2 = 22w – 2w+1 + 1
  Two’s complement min (negative): Up to 2w-1 bits
    Result range: x * y ≥ (–2w–1)*(2w–1–1) = –22w–2 + 2w–1
  Two’s complement max (positive): Up to 2w bits, but only for (TMinw)2
    Result range: x * y ≤ (–2w–1)2 = 22w–2
So, maintaining exact results…
  would need to keep expanding word size with each product computed is done in software, if needed
    e.g., by “arbitrary precision” arithmetic packages

## Slide 44
Unsigned Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
Implements Modular Arithmetic
  UMultw(u , v) = u · v mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
UMultw(u , v)
• • •

## Slide 45
Properties of Unsigned Arithmetic
Unsigned Multiplication with Addition Forms Commutative Ring
  Addition is commutative group
  Closed under multiplication
    0  UMultw(u , v)  2w –1
  Multiplication Commutative
    UMultw(u , v) = UMultw(v , u)
  Multiplication is Associative
    UMultw(t, UMultw(u , v)) = UMultw(UMultw(t, u ), v)
  1 is multiplicative identity
    UMultw(u , 1) = u
  Multiplication distributes over addtion
    UMultw(t, UAddw(u , v)) = UAddw(UMultw(t, u ), UMultw(t, v))

## Slide 46
Signed Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
  Some of which are different for signed vs. unsigned multiplication
  Lower bits are the same
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
TMultw(u , v)
• • •

## Slide 47
Properties of Two’s Comp. Arithmetic
Isomorphic Algebras
  Unsigned multiplication and addition
    Truncating to w bits
  Two’s complement multiplication and addition
    Truncating to w bits
Both Form Rings
  Isomorphic to ring of integers mod 2w
Comparison to (Mathematical) Integer Arithmetic
  Both are rings
  Integers obey ordering properties, e.g.,
    u > 0  u + v > v
    u > 0, v > 0  u · v > 0
  These properties are not obeyed by two’s comp. arithmetic
    TMax + 1 == TMin
    15213 * 30426 == -10030 (16-bit words)

## Slide 48
Power-of-2 Multiply with Shift
Operation
  u << k gives u * 2k
  Both signed and unsigned
Examples
  u << 3 == u * 8
  (u << 5) – (u << 3) == u * 24
  Most machines shift and add faster than multiply
  Compiler generates this code automatically
• • •
0
0
1
0
0
0
•••
u
2k
*
u · 2k
True Product: w+k bits
Operands: w bits
Discard k bits: w bits
UMultw(u , 2k)
•••
• • •
0
0
0
•••
TMultw(u , 2k)
0
0
0
•••
•••

## Slide 49
Unsigned Power-of-2 Divide with Shift
Quotient of Unsigned by Power of 2
u >> k gives  u / 2k 
Uses logical shift
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
0
0
•••
•••
 u / 2k 
•••
Result:
.
Binary Point
0
0
0
0
•••
0

## Slide 50
Signed Power-of-2 Divide with Shift
Quotient of Signed by Power of 2
  x >> k gives  x / 2k 
  Uses arithmetic shift
  Rounds wrong direction when u < 0
0
0
1
0
0
0
•••
x
2k
/
x / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
•••
•••
RoundDown(x / 2k)
•••
Result:
.
Binary Point
0
•••

## Slide 51
Correct Power-of-2 Divide
Quotient of Negative Number by Power of 2
  Want  x / 2k  (Round Toward 0)
  Compute as  (x+2k-1)/ 2k 
  In C: (x + (1<<k)-1) >> k
  Biases dividend toward 0
Case 1: No rounding
Divisor:
Dividend:
0
0
1
0
0
0
•••
u
2k
/
 u / 2k 
•••
k
1
•••
0
0
0
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
1
1
•••
1
•••
1
1
1
•••
    Biasing has no effect

## Slide 52
Mathematical Properties
Case 2: Rounding
Divisor:
Dividend:
0
0
1
0
0
0
•••
x
2k
/
 x / 2k 
•••
k
1
•••
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
•••
•••
    Biasing adds 1 to final result
•••
Incremented by 1
Incremented by 1

## Slide 53
Arithmetic: Basic Rules
Addition:
  Unsigned/signed: Normal addition followed by truncate, same operation on bit level
  Unsigned: addition mod 2w
    Mathematical addition + possible subtraction of 2w
  Signed: modified addition mod 2w (result in proper range)
    Mathematical addition + possible addition or subtraction of 2w
Multiplication:
  Unsigned/signed: Normal multiplication followed by truncate, same operation on bit level
  Unsigned: multiplication mod 2w
  Signed: modified multiplication mod 2w (result in proper range)

## Slide 54
Arithmetic: Basic Rules
Unsigned ints, 2’s complement ints are isomorphic rings: isomorphism = casting
Left shift
  Unsigned/signed: multiplication by 2k
  Always logical shift
Right shift
  Unsigned: logical shift, div (division + round to zero) by 2k
  Signed: arithmetic shift
    Positive numbers: div (division + round to zero) by 2k
    Negative numbers: div (division + round away from zero) by 2k Use biasing to fix

## Slide 55
Why Should I Use Unsigned?
Don’t use without understanding implications
  Easy to make mistakes
unsigned i;
for (i = cnt-2; i >= 0; i--)
a[i] += a[i+1];
Can be very subtle
#define DELTA sizeof(int)
int i;
for (i = CNT; i-DELTA >= 0; i-= DELTA)
. . .

## Slide 56
Counting Down with Unsigned
Proper way to use unsigned as loop index
unsigned i;
for (i = cnt-2; i < cnt; i--)
a[i] += a[i+1];
See Robert Seacord, Secure Coding in C and C++
  C Standard guarantees that unsigned addition will behave like modular arithmetic
    0 – 1  UMax
Even better
size_t i;
for (i = cnt-2; i < cnt; i--)
a[i] += a[i+1];
  Data type size_t defined as unsigned value with length = word size
  Code will work even if cnt = UMax
  What if cnt is signed and < 0?

## Slide 57
Why Should I Use Unsigned? (cont.)
Do Use When Performing Modular Arithmetic
  Multiprecision arithmetic
Do Use When Using Bits to Represent Sets
  Logical right shift, no sign extension

## Slide 58
Fractional Binary Numbers
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
• • •

## Slide 59
Fractional Binary Numbers: Examples
Value Representation
5 3/4 101.112
2 7/8 010.1112
1 7/16 001.01112
Observations
  Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
    Use notation 1.0 – ε

## Slide 60
Representable Numbers
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits
  Limited range of numbers (very small values? very large?)

## Slide 61
IEEE Floating Point
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard

## Slide 62
Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac

## Slide 63
Precision options
Single precision: 32 bits
Double precision: 64 bits
Extended precision: 80 bits (Intel only)
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits
s | exp | frac
1 | 15-bits | 63 or 64-bits

## Slide 64
“Normalized” Values
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value: E = Exp – Bias
  Exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (Exp: 1…254, E: -126…127)
    Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
  Minimum when frac=000…0 (M = 1.0)
  Maximum when frac=111…1 (M = 2.0 – ε)
  Get extra leading bit for “free”
v = (–1)s M 2E

## Slide 65
s
exp
frac
Normalized Encoding Example
Value: float F = 15213.0;
1521310 = 111011011011012
  = 1.11011011011012 x 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  Exp = 140 = 100011002
Result: 0 1 0 0 0 1 1 0 0 1 1 0 1 1 0 1 1 0 1 1 0 1 0 0 0 0 0 0 0 0 0 0
v = (–1)s M 2E
E = Exp – Bias

## Slide 66
Denormalized Values
Condition: exp = 000…0
Exponent value: E = 1 – Bias (instead of E = 0 – Bias)
Significand coded with implied leading 0: M = 0.xxx…x2
xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (why?)
  exp = 000…0, frac ≠ 000…0
    Numbers closest to 0.0
    Equispaced
v = (–1)s M 2E
E = 1 – Bias

## Slide 67
Examples
#include <iostream>
#include <string>
using namespace std;
int main() {
const float x=1.1;
const float z=1.123;
float y=x;
for(int j=0;j<90000000;j++)
{
y*=x;
y/=z;
y+=0;
y-=0;
}
return 0;
}
#include <iostream>
#include <string>
using namespace std;
int main() {
const float x=1.1;
const float z=1.123;
float y=x;
for(int j=0;j<90000000;j++)
{
y*=x;
y/=z;
y+=0.1f;
y-=0.1f;
}
return 0;
}
code1.c
code2.c

## Slide 68
Special Values
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = + , 1.0/−0.0 = − 
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  −  ,   0

## Slide 69
Visualization: Floating Point Encodings
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 70
Tiny Floating Point Example
8-bit Floating Point Representation
  the sign bit is in the most significant bit
  the next four bits are the exponent, with a bias of 7
  the last three bits are the frac
Same general form as IEEE Format
  normalized, denormalized
  representation of 0, NaN, infinity
s | exp | frac
1 | 4-bits | 3-bits

## Slide 71
Visualization: Floating Point Encodings
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias

## Slide 72
Distribution of Values
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 23-1-1 = 3
Notice how the distribution gets denser toward zero.
s | exp | frac
1 | 3-bits | 2-bits
8 values

## Slide 73
Distribution of Values (close-up view)
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 3
s | exp | frac
1 | 3-bits | 2-bits

## Slide 74
Special Properties of the IEEE Encoding
FP Zero Same as Integer Zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider −0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield?
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity

## Slide 75
Floating Point Operations: Basic Idea
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent too large
    Possibly round to fit into frac
x +f y = Round(x + y)
x f y = Round(x  y)

## Slide 76
Rounding
Rounding Modes (illustrate with $ rounding)
$1.40 $1.60 $1.50 $2.50 –$1.50
Towards zero $1 $1 $1 $2 –$1
Round down (−) $1 $1 $1 $2 –$2
Round up (+) $2 $2 $2 $3 –$1
Nearest Even (default) $1 $2 $2 $2 –$2

## Slide 77
Closer Look at Round-To-Even
Default Rounding Mode
  Hard to get any other kind without dropping into assembly
  All others are statistically biased
Sum of set of positive numbers will consistently be over- or under- estimated
Applying to Other Decimal Places / Bit Positions
  When exactly halfway between two possible values
  Round so that least significant digit is even
  E.g., round to nearest hundredth
7.8949999 7.89 (Less than half way)
7.8950001 7.90 (Greater than half way)
7.8850000 7.90 (Half way—round up)
7.8850000 7.88 (Half way—round down)

## Slide 78
Rounding Binary Numbers
Binary Fractional Numbers
  “Even” when least significant bit is 0
  “Half way” when bits to right of rounding position = 100…2
Examples
  Round to nearest 1/4 (2 bits right of binary point)
Value Binary Rounded Action Rounded Value
2 3/32 10.000112 10.002 (<1/2—down) 2
2 3/16 10.001102 10.012 (>1/2—up) 2 ¼
2 7/8 10.111002 11.002 ( 1/2—up) 3
2 5/8 10.101002 10.102 ( 1/2—down) 2 1/2

## Slide 79
FP Multiplication
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands

## Slide 80
Floating Point Addition
(–1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up

## Slide 81
Compare to those of Abelian Group
  Closed under addition?
    But may generate infinity or NaN
  Commutative?
  Associative?
    Overflow and inexactness of rounding
    (3.14+1e10)-1e10 = 0, 3.14+(1e10-1e10) = 3.14
  0 is additive identity?
  Every element has additive inverse?
    Yes, except for infinities & NaNs
Monotonicity
  a ≥ b ⇒ a+c ≥ b+c?
    Except for infinities & NaNs
Mathematical Properties of FP Add
Yes
Yes
Yes
No
Almost
Almost

## Slide 82
Mathematical Properties of FP Mult
Compare to Commutative Ring
  Closed under multiplication?
    But may generate infinity or NaN
  Multiplication Commutative?
  Multiplication is Associative?
    Possibility of overflow, inexactness of rounding
    Ex: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  1 is multiplicative identity?
  Multiplication distributes over addition?
    Possibility of overflow, inexactness of rounding
    1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN
Monotonicity
  a ≥ b & c ≥ 0 ⇒ a * c ≥ b *c?
    Except for infinities & NaNs
Yes
Yes
No
Yes
No
Almost

## Slide 83
Floating Point in C
C Guarantees Two Levels
float single precision
float double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode

## Slide 84
Floating Point Puzzles
For each of the following C expressions, either:
  Argue that it is true for all argument values
  Explain why not true
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (double)(float) d
f == -(-f);
2/3 == 2/3.0
d < 0.0 ⇒ ((d*2) < 0.0)
d > f ⇒ -f > -d
d * d >= 0.0
(d+f)-d == f
int x = …;
float f = …;
double d = …;
Assume neither
d nor f is NaN

## Slide 85
Summary
IEEE Floating Point has clear mathematical properties
Represents numbers of form M x 2E
One can reason about operations independent of implementation
As if computed with perfect precision and then rounded
Not the same as real arithmetic
Violates associativity/distributivity
Makes life difficult for compilers & serious numerical applications programmers

## Slide 86
Creating Floating Point Number
Steps
  Normalize to have leading 1
  Round to fit within fraction
  Postnormalize to deal with effects of rounding
Case Study
  Convert 8-bit unsigned numbers to tiny floating point format
Example Numbers
  128 10000000
  15 00001101
  33 00010001
  35 00010011
  138 10001010
  63 00111111
s | exp | frac
1 | 4-bits | 3-bits

## Slide 87
Normalize
Requirement
  Set binary point so that numbers of form 1.xxxxx
  Adjust all to have leading one
    Decrement exponent as shift left
  Value Binary Fraction Exponent
  128 10000000 1.0000000 7
  15 00001101 1.1010000 3
  17 00010001 1.0001000 4
  19 00010011 1.0011000 4
  138 10001010 1.0001010 7
  63 00111111 1.1111100 5
s | exp | frac
1 | 4-bits | 3-bits

## Slide 88
Rounding
Round up conditions
  Round = 1, Sticky = 1 ➙ > 0.5
  Guard = 1, Round = 1, Sticky = 0 ➙ Round to even
  Value Fraction GRS Incr? Rounded
  128 1.0000000 000 N 1.000
  15 1.1010000 100 N 1.101
  17 1.0001000 010 N 1.000
  19 1.0011000 110 Y 1.010
  138 1.0001010 011 Y 1.001
  63 1.1111100 111 Y 10.000
1.BBGRXXX
Guard bit: LSB of result
Round bit: 1st bit removed
Sticky bit: OR of remaining bits

## Slide 89
Postnormalize
Issue
  Rounding may have caused overflow
  Handle by shifting right once & incrementing exponent
  Value Rounded Exp Adjusted Result
  128 1.000 7 128
  15 1.101 3 15
  17 1.000 4 16
  19 1.010 4 20
  138 1.001 7 134
  63 10.000 5 1.000/6 64

## Slide 90
Interesting Numbers
Description exp frac Numeric Value
Zero 00…00 00…00 0.0
Smallest Pos. Denorm. 00…00 00…01 2–{23,52} x 2–{126,1022}
  Single ≈ 1.4 x 10–45
  Double ≈ 4.9 x 10–324
Largest Denormalized 00…00 11…11 (1.0 – ε) x 2–{126,1022}
  Single ≈ 1.18 x 10–38
  Double ≈ 2.2 x 10–308
Smallest Pos. Normalized 00…01 00…00 1.0 x 2–{126,1022}
  Just larger than largest denormalized
One 01…11 00…00 1.0
Largest Normalized 11…10 11…11 (2.0 – ε) x 2{127,1023}
  Single ≈ 3.4 x 1038
  Double ≈ 1.8 x 10308
{single,double}

## Slide 91
Byte-Oriented Memory Organization
Programs refer to data by address
  Conceptually, envision it as a very large array of bytes
    In reality, it’s not, but can think of it that way
  An address is like an index into that array
    and, a pointer variable stores an address
Note: system provides private address spaces to each “process”
  Think of a process as a program being executed
  So, a program can clobber its own data, but not that of others
• • •
00•••0
FF•••F

## Slide 92
Machine Words
Any given computer has a “Word Size”
  Nominal size of integer-valued data
    and of addresses
  Until recently, most machines used 32 bits (4 bytes) as word size
    Limits addresses to 4GB (232 bytes)
  Increasingly, machines have 64-bit word size
    Potentially, could have 18 EB (exabytes) of addressable memory
    That’s 18.4 X 1018
  Machines still support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes

## Slide 93
Word-Oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 94
Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | − | − | 10/16
pointer | 4 | 8 | 8

## Slide 95
Byte Ordering
So, how are the bytes within a multi-byte word ordered in memory?
Conventions
  Big Endian: Sun, PPC Mac, Internet
    Least significant byte has highest address
  Little Endian: x86, ARM processors running Android, iOS, and Windows
    Least significant byte has lowest address

## Slide 96
Byte Ordering Example
Example
  Variable x has 4-byte value of 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 97
Representing Integers
Decimal: 15213
Binary: 0011 1011 0110 1101
Hex: 3 B 6 D
6D
3B
00
00
IA32, x86-64
3B
6D
00
00
Sun
int A = 15213;
93
C4
FF
FF
IA32, x86-64
C4
93
FF
FF
Sun
Two’s complement representation
int B = -15213;
long int C = 15213;
00
00
00
00
6D
3B
00
00
x86-64
3B
6D
00
00
Sun
6D
3B
00
00
IA32

## Slide 98
Examining Data Representations
Code to Print Byte Representation of Data
  Casting pointer to unsigned char * allows treatment as a byte array
Printf directives:
%p: Print pointer
%x: Print Hexadecimal
typedef unsigned char *pointer;
void show_bytes(pointer start, size_t len){
size_t i;
for (i = 0; i < len; i++)
printf("%p\t0x%.2x\n",start+i, start[i]);
printf("\n");
}

## Slide 99
show_bytes Execution Example
int a = 15213;
printf("int a = 15213;\n");
show_bytes((pointer) &a, sizeof(int));
Result (Linux x86-64):
int a = 15213;
0x7fffb7f71dbc 6d
0x7fffb7f71dbd 3b
0x7fffb7f71dbe 00
0x7fffb7f71dbf 00

## Slide 100
Representing Pointers
Different compilers & machines assign different locations to objects
Even get different results each time run program
int B = -15213;
int *P = &B;
x86-64
Sun
IA32
EF
FF
FB
2C
AC
28
F5
FF
3C
1B
FE
82
FD
7F
00
00

## Slide 101
Representing Strings
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Character “0” has code 0x30
      Digit i has code 0x30+i
  String should be null-terminated
    Final character = 0
Compatibility
  Byte ordering not an issue
char S[6] = "18213";
IA32
Sun
31
38
32
31
33
00
31
38
32
31
33
00

## Slide 102
ASCII Table

## Slide 103
Compiled Multiplication Code
C compiler automatically generates shift/add code when multiplying by constant
leaq (%rax,%rax,2), %rax
salq $2, %rax
long mul12(long x)
{
return x*12;
}
t <- x+x*2
return t << 2;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 104
Compiled Unsigned Division Code
Uses logical shift for unsigned
For Java Users
  Logical shift written as >>>
shrq $3, %rax
unsigned long udiv8
(unsigned long x)
{
return x/8;
}
# Logical shift
return x >> 3;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 105
Compiled Signed Division Code
testq %rax, %rax
js L4
L3:
sarq $3, %rax
ret
L4:
addq $7, %rax
jmp L3
Uses arithmetic shift for int
For Java Users
  Arith. shift written as >>
long idiv8(long x)
{
return x/8;
}
if x < 0
x += 7;
# Arithmetic shift
return x >> 3;
Compiled Arithmetic Operations
Explanation