## Slide 1: 计算机组成与系统结构 Computer Organization & System Architecture
Huang Kejie (黄科杰) 百人计划研究员
Office: 玉泉校区老生仪楼304
Email address: huangkejie@zju.edu.cn
HP: 17706443800

## Slide 2
Recap: Complete RV32I ISA

## Slide 3
State Required by RV32I ISA
Each instruction reads and updates this state during execution:
Registers (x0..x31)
  Register file (or regfile) Reg holds 32 registers x 32 bits/register: Reg[0].. Reg[31]
  First register read specified by rs1 field in instruction
  Second register read specified by rs2 field in instruction
  Write register (destination) specified by rd field in instruction
  x0 is always 0 (writes to Reg[0] are ignored)
Program Counter (PC)
  Holds address of current instruction
Memory (MEM)
  Holds both instructions & data, in one 32-bit byte-addressed memory space
  We’ll use separate memories for instructions (IMEM) and data (DMEM)
    Later we’ll replace these with instruction and data caches
  Instructions are read (fetched) from instruction memory (assume IMEM read-only)
  Load/store instructions access data memory

## Slide 4
One-Instruction-Per-Cycle RISC-V Machine
Reg[]
pc
IMEM
DMEM
Combinational Logic
clock
On every tick of the clock, the computer executes one instruction
Current state outputs drive the inputs to the combinational logic, whose outputs settles at the values of the state before the next clock edge
At the rising clock edge, all the state elements are updated with the combinational logic outputs, and execution moves to the next clock cycle

## Slide 5
Basic Phases of Instruction Execution
IMEM
+4
rs2
rs1
rd
Reg[]
ALU
DMEM
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
mux
Clock
time

## Slide 6
Implementing the add instruction
RISC-V Assembly Instruction:
add rd, rs1, rs2
Instruction makes two changes to machine’s state:
  Reg[rd] = Reg[rs1] + Reg[rs2]
  PC = PC + 4

## Slide 7
Datapath for add

## Slide 8
Timing Diagram for add
clock
1000
1004
PC
1004
1008
PC+4
add x1,x2,x3
add x6,x7,x9
inst[31:0]
Clock
time
Reg[2]
Reg[7]
Reg[rs1]
Reg[2]+Reg[3]
alu
Reg[7]+Reg[9]
Reg[3]
Reg[9]
Reg[rs2]
???
Reg[1]
Reg[2]+Reg[3]

## Slide 9
Implementing the sub instruction
RISC-V Assembly Instruction:
sub rd, rs1, rs2
Almost the same as add, except now have to subtract operands instead of adding them
inst[30] selects between add and subtract

## Slide 10
Datapath for add/sub

## Slide 11
Implementing other R-Format instructions
All implemented by decoding funct3 and funct7 fields and selecting appropriate ALU function

## Slide 12
Implementing the addi instruction
RISC-V Assembly Instruction:
addi x15,x1,-50
111111001110
00001
000
01111
0010011
OP-Imm
rd=15
ADD
imm=-50
rs1=1

## Slide 13
Datapath for add/sub

## Slide 14
Adding addi to datapath
Also works for all other I-format arithmetic instruction (slti,sltiu,andi,ori,xori,slli,srli,srai) just by changing ALUSel

## Slide 15
I-Format immediates
High 12 bits of instruction (inst[31:20]) copied to low 12 bits of immediate (imm[11:0])
Immediate is sign-extended by copying value of inst[31] to fill the upper 20 bits of the immediate value (imm[31:12])
inst[31:0]
------inst[31]-(sign-extension)-------
inst[30:20]
imm[31:0]
Imm.
Gen
inst[31:20]
imm[31:0]
ImmSel=I

## Slide 16
Implementing Load Word instruction
RISC-V Assembly Instruction:
lw x14, 8(x2)
000000001000
00010
010
01110
0000011
LOAD
rd=14
LW
imm=+8
rs1=2

## Slide 17
Adding addi to datapath

## Slide 18
Adding lw to datapath

## Slide 19
All RV32 Load Instructions
Supporting the narrower loads requires additional circuits to extract the correct byte/halfword from the value loaded from memory, and sign- or zero-extend the result to 32 bits before writing back to register file.
funct3 field encodes size and signedness of load data

## Slide 20
Implementing Store Word instruction
RISC-V Assembly Instruction:
sw x14, 8(x2)
0000000
01110
00010
010
01000
0100011
STORE
offset[4:0]
=8
SW
offset[11:5]
=0
rs2=14
rs1=2
combined 12-bit offset = 8
0000000
01000

## Slide 21
Adding lw to datapath

## Slide 22
Adding sw to datapath

## Slide 23
I-Format immediates
High 12 bits of instruction (inst[31:20]) copied to low 12 bits of immediate (imm[11:0])
Immediate is sign-extended by copying value of inst[31] to fill the upper 20 bits of the immediate value (imm[31:12])
inst[31:0]
------inst[31]-(sign-extension)-------
inst[30:20]
imm[31:0]
Imm.
Gen
inst[31:20]
imm[31:0]
ImmSel=I

## Slide 24
I-Format immediates
Just need a 5-bit mux to select between two positions where low five bits of immediate can reside in instruction
Other bits in immediate are wired to fixed positions in instruction
imm[11:5]
rs2
rs1
funct3
imm[4:0]
S-opcode
imm[11:0]
rs1
funct3
rd
I-opcode
inst[31](sign-extension)
inst[30:25]
imm[31:0]
inst[31:0]
inst[24:20]
S
I
inst[31](sign-extension)
inst[30:25]
inst[11:7]
0
6
7
11
12
14
15
19
20
24
25
31
0
4
5
10
11
31
1
6
5
5
S
I

## Slide 25
Implementing Branches
B-format is mostly same as S-Format, with two register sources (rs1/rs2) and a 12-bit immediate
But now immediate represents values -4096 to +4094 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)

## Slide 26
Adding sw to datapath

## Slide 27
Adding branches to datapath

## Slide 28
Branch Comparator
BrEq = 1, if A=B
BrLT = 1, if A < B
BrUn =1 selects unsigned comparison for BrLT, 0=signed
BGE branch: A >= B, if !(A<B)
Branch Comp.
A
B
BrUn
BrEq
BrLT

## Slide 29
Multiply Branch Immediates by Shift?
12-bit immediate encodes PC-relative offset of -4096 to +4094 bytes in multiples of 2 bytes
Standard approach: treat immediate as in range -2048..+2047, then shift left by 1 bit to multiply by 2 for branches
s
rs2
rs1
funct3
imm[4:0]
B-opcode
imm[10:5]
s
imm[10:5]
imm[4:0]
s
imm[10:5]
imm[4:0]
0
sign-extension
sign-extension
S-Immediate
B-Immediate (shift left by 1)
Each instruction immediate bit can appear in one of two places in output immediate value – so need one 2-way mux per bit

## Slide 30
RISC-V Branch Immediates
12-bit immediate encodes PC-relative offset of -4096 to +4094 bytes in multiples of 2 bytes
RISC-V approach: keep 11 immediate bits in fixed position in output value, and rotate LSB of S-format to be bit 12 of B-format
sign=imm[11]
imm[10:5]
imm[4:0]
sign=imm[12]
imm[10:5]
imm[4:1]
0
S-Immediate
B-Immediate (shift left by 1)
Only one bit changes position between S and B, so only need a single-bit 2-way mux
imm[11]

## Slide 31
RISC-V Immediate Encoding
Instruction Encodings, inst[31:0]
32-bit immediates produced, imm[31:0]
Only bit 7 of instruction changes role in immediate between S and B
Upper bits sign-extended from inst[31] always

## Slide 32
Implementing JALR Instruction (I-Format)
JALR rd, rs, immediate
  Writes PC+4 to Reg[rd] (return address)
  Sets PC = Reg[rs1] + immediate
  Uses same immediates as arithmetic and loads
    no multiplication by 2 bytes

## Slide 33
Adding branches to datapath

## Slide 34
Adding jalr to datapath

## Slide 35
Implementing jal Instruction (I-Format)
JAL saves PC+4 in Reg[rd] (the return address)
Set PC = PC + offset (PC-relative jump)
Target somewhere within ±219 locations, 2 bytes apart
  ±218 32-bit instructions
Immediate encoding optimized similarly to branch instruction to reduce hardware cost

## Slide 36
Adding jal to datapath

## Slide 37
“Upper Immediate” instructions
Has 20-bit immediate in upper 20 bits of 32-bit instruction word
One destination register, rd
Used for two instructions
  LUI – Load Upper Immediate (add to zero)
  AUIPC – Add Upper Immediate to PC

## Slide 38
Implementing lui

## Slide 39
Implementing auipc

## Slide 40
Single-Cycle RISC-V RV32I Datapath

## Slide 41
And in Conclusion, …
Universal datapath
  Capable of executing all RISC-V instructions in one cycle each
  Not all units (hardware) used by all instructions
5 Phases of execution
  IF, ID, EX, MEM, WB
  Not all instructions are active in all phases
Controller specifies how to execute instructions
  what new instructions can be added with just most control?